## Slide 1: Unit II
Mobile Network Layer
By : Prof Nilam S. Honmane
ZCOER,Pune

## Slide 2: Contents
Mobile IP: Goals, assumptions and requirements, Entities and Terminology, IP packet delivery, Agent advertisement and discovery, Registration, Tunnelling and Encapsulation, Optimizations, Reverse tunnelling,
IPv6:DHCP, AdHoc networks: Routing, Proactive protocol-DSDV
Reactive Routing Protocols: DSR, AODV, Hybrid routing –ZRP
Multicast Routing: ODMRP, Vehicular Ad Hoc networks (VANET) MANET Vs VANET Security.

## Slide 3: MOBILE INTERNET PROTOCOL AND TRANSPORT LAYER
Overview of Mobile IP – Features of Mobile IP – Key Mechanism in Mobile IP – route Optimization. Overview of TCP/IP – Architecture of TCP/IP- Adaptation of TCP Window – Improvement in TCP Performance.
2

## Slide 4: Why Mobile IP?
What do cellular networks and wireless LANs provide?
  Wireless connectivity
  Mobility at the data link layer
What is Dynamic Host Configuration Protocol (DHCP)?
  It provides local IP addresses for mobile hosts
  Is not secure
  Does not maintain network connectivity when moving around
What they do not provide:
  Transparent connectivity at the network layer
  Mobility with local access
  The difference between mobility and nomadicity!
3

## Slide 5: What is Mobile IP?
Mobile IP provides network layer mobility
Provides seamless roaming
‘‘Extends’’ the home network over the entire Internet
4

## Slide 6: IP Overview (1/3)
IP Addressing :
  Dotted Decimal Notation: 32 bits (4x8) used to represent IPv4 addresses - 192.19.241.18
  Network Prefix and Host Portions: p - prefix, h - host, p + h = 32. If p = 24 then h = 32 - 24 = 8. Using above address the network prefix will be
192.19.241 and host will be 18. For those of you familiar with subnet masks, “p” represents the number of 1’s in the subnet mask. If p = 24, subnet mask is 255.255.255.0, if p = 26, subnet mask is 255.255.255.192.
5

## Slide 7: IP Overview
IP Routing:
  Network prefix is used for routing. Routing tables are used to look
up next hop and the interface on the router that is to be used.
  In the routing tables we use the following notation: target/prefix length, e.g., 192.19.241.0/24, or 192.19.241.192/26.
  If two subnet masks/prefixes fit the address, the one with the largest prefix is chosen for routing. E.g., a router with the following 3 entries in its table: 7.7.7.99/32 (p=32 host specific) and 7.7.7.0/24 (0<p<32 network prefix) and 0.0.0.0/0 (p=0 default) will use entry 2 for an IP packet with destination 7.7.7.1 and entry 3 for destination 192.33.14.12.
6

## Slide 8: IP Overview
Domain Name System (DNS): used to translate a host name to an IP address. A host sends a query to a server to obtain the IP address of a destination of which it only has the host name.
Link Layer Addresses - Address Resolution Protocol (ARP):
  Once a host has the IP address of a destination it then needs to finds its layer 2 address or the layer 2 address of the next hop on the path. A broadcast message is sent and the targeted host responds with its layer 2 address.
  A proxy ARP is a response by a node for another node that cannot respond at the time the request is made (e.g. the node is a mobile node and not on its host net at the time, its home agent will respond in its stead).
  A gratuitous ARP, is a reply to no ARP request, used by a node that just joins the network and wants to make its address known. Can be used by a mobile node upon its return to its home net.
7

## Slide 9: MOtivation for Mobile IP
IP Routing
  based on IP destination address, network prefix (e.g. 129.13.42) determines physical subnet
  change of physical subnet implies change of IP address to have a topologically correct address (standard IP) or needs special entries in the routing tables
Specific routes to end-systems?
  requires changing all routing table entries to forward packets to the right destination
  does not scale with the number of mobile hosts and frequent changes in the location,security problems
Changing the IP-address?
  adjust the host IP address depending on the current location
  almost impossible to find a mobile system, DNS updates take long time
  TCP connections break, security problems
8

## Slide 10: What Mobile IP does?
Mobile IP solves the following problems:
  if a node moves without changing its IP address it will be unable to receive its packets,
  if a node changes its IP address it will have to terminate and restart its ongoing connections everytime it moves to a new network area (new network prefix).
Mobile IP is a routing protocol with a very specific purpose.
Mobile IP is a network layer solution to node mobility in the Internet.
Mobile IP is not a complete solution to mobility, changes to the transport protocols need to be made for a better solution (i.e., the transport layers are unaware of the mobile node’s point of attachment and it might be useful if, e.g., TCP knew that a wireless link was being used!).
9

## Slide 11
Requirements to Mobile IP
Transparency
  mobile end-systems keep their IP address
  continuation of communication after interruption of link possible
  point of connection to the fixed network can be changed
Compatibility
  support of the same layer 2 protocols as IP
  no changes to current end-systems and routers required
  mobile end-systems can communicate with fixed systems
Security
  authentication of all registration messages
Efficiency and scalability
  only little additional messages to the mobile system required
(connection typically via a low bandwidth radio link)
  world-wide support of a large number of mobile systems in the whole Internet
10

## Slide 12: Mobile IP Terminology
Mobile Node (MN)
  system (node) that can change the point of connection to the network without changing its IP address
Home Agent (HA)
  system in the home network of the MN, typically a router
  registers the location of the MN, tunnels IP datagrams to the COA
Foreign Agent (FA)
  system in the current foreign network of the MN, typically a router
forwards the tunneled datagrams to the MN, typically also the default router for the MN
Care-of Address (COA)
  address of the current tunnel end-point for the MN (at FA or MN)
  actual location of the MN from an IP point of view
  can be chosen, e.g., via DHCP
Correspondent Node (CN)
  communication partner
11

## Slide 13: Properties of COA
A care-of address is an IP address associated with mobile node that is visiting a foreign link:
  A care-of address is specific to the foreign link currently being visited by a mobile node
  Generally changes every time the mobile node moves from one foreign link to another
  No Mobile IP-specific procedures are needed in order to
deliver packets to a care-of address
  Is used as the exit-point of a tunnel from the home agent toward the mobile node
  Is never returned by DNS when another node looks up the
mobile node’s hostname

## Slide 14
COA
CN
router HA
router FA
Internet
router
1.
2.
3.
home network
MN
foreign network
4.
CN
router HA
router FA
Internet
router
home network
MN
foreign network
COA

## Slide 15: Types of COA
A foreign agent care-of address is an IP address of a foreign agent which has an interface on the foreign link being visited by a mobile node. Can be shared by many mobile nodes simultaneously
A collocated care-of address is an IP address temporarily assigned to an interface of the mobile node itself. The network-prefix of a collocated care-of address must equal the network-prefix that has been assigned to the foreign link being visited by a mobile node. This type of c/o address might be used by mobile node in situations where no foreign agents are available on a foreign link. A collocated c/o address can be used by only one mobile node at a time

## Slide 16: Mobile IP Features
Allows a host to be reachable at the same address, even as it changes its location
makes it seem as one network extends over the entire Internet
continuous connectivity, seamless roaming even while network applications are running
fully transparent to the user

## Slide 17: Example network
mobile end-syste
Internet
router
router
router
end-system
FA
HA
MN
home network
foreign
network
(physical home network for the MN)
(current physical network for the MN)
CN

## Slide 18: KEy Mechanism in Mobile IP
Home Agents and Foreign Agents advertise their presence on any attached links by periodically multicasting or broadcasting special Mobile IP messages called Agent Advertisements
examine their contents to determine whether they
Mobile Nodes listen to these Agent Advertisements and
are
connected to their home link or a foreign link
A Mobile Node connected to a foreign link acquires a care-of address. A foreign agent care-of address can be read from one of the fields within the foreign agent’s Agent Advertisement. A collocated care-of address must be acquired by some assignment procedure, such as Dynamic Host Configuration Protocol (DHCP), the Point-to-Point Protocol’s IP Control Protocol (IPCP), or manual configuration

## Slide 19: DATA transfer to the mobile system
Internet
sender
FA
HA
MN
home network
foreign
network
receiver
1
2
3
Sender sends to the IP address of MN, HA intercepts packet (proxy ARP)
HA tunnels packet to COA, here FA, by encapsulation
FA forwards the packet to the MN
CN

## Slide 20: DATA Transfer from the mobile system
Internet
receiver
FA
HA
MN
home network
foreign
network
sender
1
1. Sender sends to the IP address of the receiver as usual,
FA works as default router
CN

## Slide 21: KEY Mechanism in Mobile IP
The mobile IP Registers the care-of address acquired previously with its home agent, using a message-exchange defined by Mobile IP. It asks for service from a Foreign Agent, if one is present on the link. In order to prevent Denial-of-Service attacks, the registration messages are required to be authenticated
The Home Agent or some other router on the home link advertises reachability to the network-prefix of the Mobile Node’s home address, thus attracting packets that are destined to the Mobile Node’s home address. The Home Agent intercepts these packets, and tunnels them to the care-of address that the mobile node registered previously
At the care-of address – at either the Foreign Agent or one of the interfaces of the mobile node itself – the original packet is extracted from the tunnel and then delivered to the Mobile Node
In the reverse direction, packets sent by the Mobile Node are routed directly to their destination, without any need for tunneling. The Foreign Agent serves as a default router for all packets generated by visiting node

## Slide 22: Route Optimization
Triangle Routing: tunneling in its simplest form has all packets go to home network (HA) and then sent to MN via a tunnel.
  This involves two IP routes that need to be set-up, one original and
the second the tunnel route.
  Causes unnecessary network overhead and adds to the latency.
Route optimization: allows the correspondent node to learn the current location of the MN and tunnel its own packets directly. Problems arise with
  mobility: correspondent node has to update/maintain its cache.
  authentication: HA has to communicate with the correspondent node to do authentication, i.e., security association is with HA not with MN.

## Slide 23
Optimization of Packet Forwarding
Change of FA
  packets on-the-fly during the change can be lost
  new FA informs old FA to avoid packet loss, old FA now forwards remaining packets to new FA
  this information also enables the old FA to release resources for the MN

## Slide 24: Change of foreign agent
CN
HA
FAold FAnew
MN
t
request update
ACK
data
data
MN changes
location
registration
data
update
ACK
data
data
warning
update
ACK
data
data
registration

## Slide 25: PROBlems with Triangle Routing
Triangle routing has the MN correspond directly with the CN using its home address as the SA
  Firewalls at the foreign network may not allow that
  Multicasting: if a MN is to participate in a multicast group, it needs to use a reverse tunnel to maintain its association with the home network.
  TTL: a MN might have a TTL that is suitable for communication when it is in its HM. This TTL may not be sufficient when moving around (longer routes possibly). When using a reverse tunnel, it only counts as a single hop. A MN does not want to change the TTL everytime it moves.
Solution: reverse tunneling

## Slide 26: ReVErse tunneling (RFC 2344)
Internet
receiver
FA
HA
MN
home network
foreign
network
sender
3
2
1
MN sends to FA
FA tunnels packets to HA
by encapsulation
HA forwards the packet to the receiver (standard case)
CN

## Slide 27: MOBILE IP with reverse tunneling
Routers accept often only “topologically correct“ addresses (firewall!)
  a packet from the MN encapsulated by the FA is now
topologically correct
Multicast and TTL problems solved
Reverse tunneling does not solve
  all problems with firewalls, the reverse tunnel can be abused to
circumvent security mechanisms (tunnel hijacking)
  optimization of data paths, i.e. packets will be forwarded through the tunnel via the HA to a sender (longer routes)
The new standard is backwards compatible
  the extensions can be implemented easily

## Slide 28: DYNAMIC Host Configuration Protocol
Application
  simplification of installation and maintenance of networked computers
  supplies systems with all necessary information, such as IP address, DNS
server address, domain name, subnet mask, default router etc.
  enables automatic integration of systems into an Intranet or the Internet, can be used to acquire a COA for Mobile IP
Client/Server-Model
  the client sends via a MAC broadcast a request to the DHCP server
(might be via a DHCP relay)
client
relay
client
server
DHCPDISCOVER
DHCPDISCOVER

## Slide 29
DHCP - Protocol Mechanisms
server (not selected)
client
server (selected)
initialization
collection of replies
selection of configuration
initialization completed
release
confirmation of configuration
delete context
determine the
configuration
DHCPDISCOVER
DHCPOFFER
DHCPACK
DHCPRELEASE
DHCPDISCOVER
DHCPOFFER
DHCPREQUEST DHCPREQUEST
(reject) (options)
determine the
configuration

## Slide 30: DHCP characteristics
Server
  several servers can be configured for DHCP, coordination not yet standardized (i.e., manual configuration)
Renewal of configurations
  IP addresses have to be requested periodically, simplified protocol
Options
time
available for routers, subnet mask, NTP (network protocol) timeserver, SLP (service location
protocol)
directory, DNS (domain name system)
Big security problems!
  no authentication of DHCP information specified

## Slide 31: Mobile IP Summary
Allows node mobility across media of similar or dissimilar types
Uses the Mobile Node’s permanent home address when it changes its point of attachment to the Internet
Not requires any hardware and software upgrades to the existing, installed base of IPv4 hosts and routers – other than those nodes specifically involved in the provision of mobility services
Mobile Node must provide strong authentication when it
informs its Home Agent of its current location
Uses tunneling to deliver packets that are destined to the Mobile Node’s home address
3 main entities: Mobile Nodes, Foreign Agents and Home
Agents
3 basic functions: Agent Discovery, Registration, Packet Routing

## Slide 32: Ad hoc networks
Standard Mobile IP needs an infrastructure
  Home Agent/Foreign Agent in the fixed network
  DNS, routing etc. are not designed for mobility
Sometimes there is no infrastructure!
  remote areas, ad-hoc meetings, disaster areas
  cost can also be an argument against an infrastructure!
Main topic: routing
  no default router available
  every node should be able to forward
A
B
C

## Slide 33: Mobile Ad Hoc Networks (MANETs)
A MANET is an autonomous collection of mobile users that communicate over relatively bandwidth constrained wireless links
Since the nodes are mobile, the network topology may change rapidly and unpredictably over time.
The network is decentralized, where all network activity including discovering the topology and delivering messages must be executed by the nodes themselves, i.e., routing functionality will be incorporated into mobile nodes.

## Slide 34: Solution: Wireless ad-hoc networks
Network without infrastructure
  Use components of participants for networking
Examples
  Single-hop: All partners max. one hop apart
    Bluetooth piconet, PDAs in a room, gaming devices…
  Multi-hop: Cover larger distances, circumvent obstacles
    Bluetooth scatternet, TETRA police network, car-to-car networks…

## Slide 35: MANET- Characteristics
Dynamic network topology
Bandwidth constraints and variable link capacity
Energy constrained nodes
Multi-hop communications
Limited security
Autonomous terminal
Distributed operation
Light-weight terminals

## Slide 36: Manet: Mobile Ad-hoc Networking
Fixed
Network
Mobile
Devices
Mobile
Router
Manet
Mobile IP,
DHCP
Router
End system

## Slide 37: Need for Ad Hoc Networks
Setting up of fixed access points and backbone infrastructure is not always viable – Infrastructure may not be present in a disaster area or war zone – Infrastructure may not be practical for short-range radios; Bluetooth (range ~ 10m)  Ad hoc networks: – Do not need backbone infrastructure support – Are easy to deploy – Useful when infrastructure is absent, destroyed or impractical

## Slide 38: Applications of MANETS
Military battlefield

## Slide 39: Origins of TCP/IP
Transmission Control Protocol/Internet Protocol (TCP/IP)
  Resulted from a coordinated effort by the U.S. Department of Defense (DOD)
Advanced Research Projects Agency (ARPA)
  Charged with creating a wide area network (WAN)
  Results were TCP/IP and ARPANET
DOD funded two projects
  The adaptation of TCP/IP to work with UNIX
  The inclusion of the TCP/IP protocol with Berkeley UNIX (BSD UNIX)

## Slide 40: Routing examples for an ad-hoc network
N1
N4
N2
N5
N3
N1
N4
N2
N5
N3
good link
weak link
time = t1
time = t2

## Slide 41: Traditional routing algorithms
Distance Vector
  periodic exchange of messages with all physical neighbors that contain information about who can be reached at what distance
  selection of the shortest path if several paths available
Link State
  periodic notification of all routers about the current state of all physical links
  router get a complete picture of the network
Example
  ARPA packet radio network (1973), DV-Routing
    every 7.5s exchange of routing tables including link quality
    updating of tables also by reception of packets
    routing problems solved with limited flooding

## Slide 42: Problems of traditional routing algorithms
Dynamics of the topology
  frequent changes of connections, connection quality, participants
Limited performance of mobile systems
  periodic updates of routing tables need energy without contributing to the transmission of user data, sleep modes difficult to realize
  limited bandwidth of the system is reduced even more due to the exchange of routing information
  links can be asymmetric, i.e., they can have a direction dependent transmission quality
Problem
  protocols have been designed for fixed networks with infrequent changes and typically assume symmetric links

## Slide 43: DSDV (Destination Sequenced Distance Vector)
Expansion of distance vector routing
Sequence numbers for all routing updates
  assures in-order execution of all updates
  avoids loops and inconsistencies
Decrease of update frequency
  store time between first and best announcement of a path
  inhibit update if it seems to be unstable (based on the stored time values)

## Slide 44: Dynamic source routing I
Split routing into discovering a path and maintainig a path
Discover a path
  only if a path for sending packets to a certain destination is needed and no path is currently available
Maintaining a path
  only while the path is in use one has to make sure that it can be used continuously
No periodic updates needed!

## Slide 45: Dynamic source routing II
Path discovery
  broadcast a packet with destination address and unique ID
  if a station receives a broadcast packet
    if the station is the receiver (i.e., has the correct destination address) then return the packet to the sender (path was collected in the packet)
    if the packet has already been received earlier (identified via ID) then discard the packet
    otherwise, append own address and broadcast packet
  sender receives packet with the current path (address list)
Optimizations
  limit broadcasting if maximum diameter of the network is known
  caching of address lists (i.e. paths) with help of passing packets
    stations can use the cached information for path discovery (own paths or paths for other hosts)

## Slide 46: Dynamic Source Routing III
Maintaining paths
  after sending a packet
    wait for a layer 2 acknowledgement (if applicable)
    listen into the medium to detect if other stations forward the packet (if possible)
    request an explicit acknowledgement
  if a station encounters problems it can inform the sender of a packet or look-up a new path locally

## Slide 47: DSR: Route Discovery
B
A
C
G
I
D
K
L
E
H
F
J
Q
P
M
N
O
R
Sending from C to O

## Slide 48
DSR: Route Discovery
Broadcast
B
A
C
G
I
D
K
L
E
H
F
J
Q
P
M
N
O
R
[O,C,4711]
[O,C,4711]

## Slide 49
DSR: Route Discovery
B
A
C
G
I
D
K
L
E
H
F
J
Q
P
M
N
O
R
[O,C/G,4711]
[O,C/G,4711]
[O,C/B,4711]
[O,C/E,4711]

## Slide 50
DSR: Route Discovery
B
A
C
G
I
D
K
L
E
H
F
J
Q
P
M
N
O
R
[O,C/G/I,4711]
[O,C/B/A,4711]
[O,C/B/D,4711]
[O,C/E/H,4711]
(alternatively: [O,C/E/D,4711])

## Slide 51
DSR: Route Discovery
B
A
C
G
I
D
K
L
E
H
F
J
Q
P
M
N
O
R
[O,C/B/D/F,4711]
[O,C/G/I/K,4711]
[O,C/E/H/J,4711]

## Slide 52
DSR: Route Discovery
B
A
C
G
I
D
K
L
E
H
F
J
Q
P
M
N
O
R
[O,C/E/H/J/L,4711]
(alternatively: [O,C/G/I/K/L,4711])
[O,C/G/I/K/M,4711]

## Slide 53
DSR: Route Discovery
B
A
C
G
I
D
K
L
E
H
F
J
Q
P
M
N
O
R
[O,C/E/H/J/L/N,4711]

## Slide 54
DSR: Route Discovery
B
A
C
G
I
D
K
L
E
H
F
J
Q
P
M
N
O
R
Path: M, K, I, G

## Slide 55
Dynamic Source Routing III
Maintaining paths
  after sending a packet
    wait for a layer 2 acknowledgement (if applicable)
    listen into the medium to detect if other stations forward the packet (if possible)
    request an explicit acknowledgement
  if a station encounters problems it can inform the sender of a packet or look-up a new path locally

## Slide 56
Clustering of ad-hoc networks
Internet
Super cluster
Cluster
Base station
Cluster head

## Slide 57: Interference-based routing
Routing based on assumptions about interference between signals
S1
N5
N3
N4
N1
N2
R1
R2
N6
N8
S2
N9
N7
neighbors
(i.e. within radio range)

## Slide 58: Examples for interference based routing
Least Interference Routing (LIR)
  calculate the cost of a path based on the number of stations that can receive a transmission
Max-Min Residual Capacity Routing (MMRCR)
  calculate the cost of a path based on a probability function of successful transmissions and interference
Least Resistance Routing (LRR)
  calculate the cost of a path based on interference, jamming and other transmissions
LIR is very simple to implement, only information from direct neighbors is necessary